## Slide 1: Modeling response uncertainty
Modeling Uncertainty in the Earth Sciences
Jef Caers
Stanford University

## Slide 2: Modeling Uncertainty in the Earth Sciences
High dimensional
Low dimensional

## Slide 3: Characteristic of Earth Science modeling
Uncertainty on “the Earth” is huge (basically infinite)
Earth models are complex and large
Building Earth models is relatively fast (CPU-wise)
Response function are often physical models (weather, climate, flow, wave propagation etc…) and can be very CPU-demanding
What do we do in such case ?

## Slide 4: Example
Response evaluation:
CPU = Hours
Earth model generation:
CPU = Minutes
Location of wells

## Slide 5: Ranking
Use an approximate physical model (proxy) to evaluate each Earth model for its response
Rank the models according to the proxy model evaluation
Select the Earth models corresponding to the quantiles evaluated with the proxy model (e.g. deciles; P10, P50, P90)
Run the actual physical model on the selected Earth models

## Slide 6: Example of ranking tool: geobodies
Earth Model
“Geobodies”

## Slide 7: Experimental Design (ED)
“Experimenter”: in our case, the person modeling
The “treatment”: the effect of some process, in our case the effect of parameter choices on the response
The “experimental units”: the objects of that treatment
What combination of parameters should we chose, if we cannot chose all possible combinations ?

## Slide 8: ED nomenclature
A factor: in our case a parameter, number = k
A level: how that parameter is discretized, number of categories = s
Full factorial design = sk combinations

## Slide 9: Example 22 factorial design
Testing rock strength
ratio = sand/shale ratio

## Slide 10: Effect estimates

## Slide 11: Type of designs
Factorial design: sk
Fractional factorial design: s(k-p)
Central composite design

## Slide 12: Fractional factorial design
Fractional factorial design 2(3-1)

## Slide 13: Response surface designs
How many pairs of PORO/PERM do I need to get this surface as accurately as possible
What combination of PORO/PERM values should I chose ?
A response surface

## Slide 14: Central composite design
Total combinations = 9
Total combinations = 15

## Slide 15: Example

## Slide 16: Effect estimates

## Slide 17: Monte Carlo simulation using the response surface
Assume the response surface is a good approximation of the actual response
Perform Monte Carlo simulation of the input parameters
For each sampled parameter set, calculate the response using the response surface

## Slide 18: Result

## Slide 19: Experimental design: example
layering
Shale
Calcite cement
Permeability
(sgsim)
From White et al, SPE Journal
Notes: An example of a complex outcrop that is modeled with shale layers as well as cementation due to bedding and continuous properties that are modeled with a variogram, the top figures show show the shale, the bottom the permeability, horizonatal and vertical

## Slide 20: Factors considered
Notes: Tha various factors considered and tre choice for low/medium/high

## Slide 21: Response evaluation
Inject tracer (a dye basically)
Check when tracer arrives
Notes: Reponse analysis is a tracer injected on the right and as response we measure the arrivalk time on the right

## Slide 22: Effects estimate
r = variogram range
n = nugget
a = anisotropy
c = cement permeability
d = shale resistance
Parameters
Effect estimate on
tracer arrival time

## Slide 23: Response surface
Tracer arrival time
Notes: Example response surface

## Slide 24: Limitations
Works well for continuous, simple parameters, e.g. permeability in channel, depth of water table, variogram range
Cannot deal with spatial uncertainty, only “input uncertainty”
Not suited for scenario parameters such as the choice of a training image or choice of scenario (with shale/without shale)
Not suited for parameters that induce a discrete and/or discontinuous change in the response

## Slide 25: Distance methods
Reponses that exhibit discrete changes
Parameters that may have major impact on uncertainty, such as the choice of a training image
Can be used with any parameters

## Slide 26: Recall chapter 9

## Slide 27: Do a simple transformation
D | 1 | 2 | 3 | 4
1 | 0 | 1 | 1 | 
2 | 1 | 0 |  | 1
3 | 1 |  | 0 | 1
4 |  | 1 | 1 | 0
D | 1 | 2 | 3 | 4
1 | 0 | 1 | 1 | 
2 | 1 | 0 |  | 1
3 | 1 |  | 0 | 1
4 |  | 1 | 1 | 0
distance
k= 1-exp(-d)
K | 1 | 2 | 3 | 4
1 | 0 | 0.86 | 0.86 | 0.94
2 | 0.86 | 0 |  | 0.86
3 | 0.86 |  | 0 | 0.86
4 |  | 0.86 | 0.86 | 0
K | 1 | 2 | 3 | 4
1 | 0 | 0.86 | 0.86 | 0.94
2 | 0.86 | 0 |  | 0.86
3 | 0.86 |  | 0 | 0.86
4 |  | 0.86 | 0.86 | 0
new distance
λ1 = λ2 = 1
λ3 = λ4 = 0
λ1 = λ2 = 0.44
λ3 = 0.31
λ4 = 0

## Slide 28: Linear separation is possible
1
2
3
4

## Slide 29: Kernel transformation
RBF Kernel
2D projection of models
From metric space
2D projection of models
in feature space
Making the map nicer and easier to work with

## Slide 30: Idea
Find models with similar responses
Group them into a single “cluster”
Select a representative model for that cluster
Evaluate uncertainty by considering only the representative models

## Slide 31: Clustering
Supervised clustering
Unsupervised clustering

## Slide 32: k-means clustering

## Slide 33: k-means versus k-medoid

## Slide 34: Kernel k-means or k-medoid clustering

## Slide 35: Clustering Earth models

## Slide 36: Case study
West-Africa deep water turbidite offshore reservoir
Dimensions of the reservoir model
  78 x 59 x 116 gridblocks
28 wells
  20 production wells (red)
  8 injection wells (blue)
1 flow simulation = 3 hours

## Slide 37: Model of spatial continuity
Uncertain about channels
Proportion
Channel width
Channel width/thickness ratio
Sinuosity

## Slide 38: Spatial uncertainty

## Slide 39: Distance
Use a fast flow simulator as an approximation
Define the distance based on the output of this fast flow simulator
Create map with MDS

## Slide 40: Kernel transformation

## Slide 41: K-medoid Clustering

## Slide 42: Response calculation
Response of 7 selected Earth models
Calculated P10, P50 and P90

## Slide 43: Experimental design

## Slide 44: Another application
Made in Patagonia
Motorola
Made in USA
Motorola
Made in USA
Samsung
Made in Patagonia
Samsung
Made in USA
Motorola
Made in Patagonia
Samsung
Production
Parameters
Produced
Model
Test
Response
MDS

## Slide 45: Sensitivity analysis
MDS
Clustering
Motorola
Made in USA
Samsung
Made in Patagonia
Samsung
Made in Patagonia
Samsung
Made in USA
Samsung
Made in USA
Motorola
Made in Patagonia

## Slide 46: Experimental design

## Slide 47: Experimental design
Channel Thickness | Width Thickness Ratio | Channel Sinuosity | % Sand | Cumulative Oil at time “36” In 104 MSTB
H | H | L | M | 8.5
H | H | H | H | 8.1
H | H | H | L | 7.6
M | L | L | M | 6.8
M | L | H | M | 6.1
L | H | L | L | 5.4
L | M | M | H | 5.1
H = High
M = Medium
L = Low

## Slide 48: Effect estimates