## Slide 1: Value of Information
ENERGY 160/260
Modeling Uncertainty in the Earth Sciences

## Slide 2: Recall our case study from lecture 1
Decision to be made:
move certain farms (or not) to protect groundwater

## Slide 3: Value of information
To determine the value of gathering data prior to actually gathering the data, this value will depend on
The particular decision problem at hand
The uncertainty prior to gathering the data
The reliability of the measurement device in resolving spatial variation or key geological drivers

## Slide 4: Simple generic example
Decision to make about an opportunity, alternatives D1 (go ahead) or D2 (walk)
Uncertain event A, possibilities a1 and a2 influence outcome in case we decide to go ahead
Do we decide between D1 and D2 or do we take more data B, whose outcome is uncertain
Two possible outcomes for data: b1 and b2

## Slide 5: Decision tree
B
B1
B2
A
A
A1|B1
A2|B1
A1|B2
A2|B2
NPV(A1)
NPV(A1)
NPV(A2)
NPV(A2)
A
a1
a2
NPV(a1)
NPV(a2)
P(A=a1)
P(A=a2)

## Slide 6: Decision tree with data
B
B=b1
B=b2
A
A
A=a1|b1
A=a2|b1
A=a1|b2
A=a2|b2
NPV(a1)
NPV(a1)
NPV(a2)
NPV(a2)
A
a1
a2
NPV(a1)
NPV(a2)
P(A=a1)
P(A=a2)

## Slide 7: Data reliability
Important in determining VOI is determining how well
the data source B will resolve the uncertain event A
A reliability is modeled as a conditional distribution of the form
P(data says | what real world is)

## Slide 8: Data reliability vs information content
A reliability is modeled as a conditional distribution of the form
P(data says | what real world is)
Information content of data is a conditional probability of the form
P(what real world is | data says)

## Slide 9: Data reliability vs information content

## Slide 10: Bayes’ rule
Calculating information content from data reliability
Because (summing over all possibilities of A)

## Slide 11: Decision tree with data
B
b1
b2
A
A
A=a1|b1
A=a2|b1
A=a1|b2
A=a2|b2
NPV(a1)
NPV(a1)
NPV(a2)
NPV(a2)
A
a1
a2
NPV(a1)
NPV(a2)
P(A=a1)
P(A2)

## Slide 12: Example: decision problem
Cleancost = 10; Penalty = 7.5, P(A=a1)=0.6; P(A=a2)=0.4

## Slide 13: Decision with the option to collect data

## Slide 14: Perfect information

## Slide 15: Result

## Slide 16: Imperfect data

## Slide 17: Result

## Slide 18: Spatial value of information problems
Previously: the uncertain event was a simple binary or categorical variable
What if the “uncertain event” is the “uncertain Earth model”
What if the data is complex such as geophysical data

## Slide 19: Two components in modeling spatial uncertainty

## Slide 20: Example case study
Coast-line
Farming area
Intrusion of sea-water due to excessive use
of groundwater for farming
Wells to extract groundwater

## Slide 21: Challenge
Intrusion of sea-water due to excessive farming
Intrusion is not “uniform”, areas which have subsurface fluvial channels have more intrusion
We don’t know exactly where channels are: uncertainty
We don’t know what the best action to take is

## Slide 22: Alternative actions
Drill wells and inject water to replenish the groundwater table and drive out the salt water
Propose three location for such recharge = three different actions + no recharge
Loc 1
Loc 2
Loc 3
which is the best location
if we can only afford one well?

## Slide 23: Recall
Spatial
Stochastic
simulator
input
Seed 1
Seed 2
Earth Models
(spatial uncertainty)
(input uncertainty)
Data
(samples, well, geophysics…)

## Slide 24: Recall
Spatial
Stochastic
simulator
input
Seed 1
Seed 2
Earth Models
(spatial uncertainty)
(input uncertainty)
Data
(samples, well, geophysics…)

## Slide 25: Formalization of VOI
Consider a case with one uncertain input parameter and with two possible choices for it
For example, you have two training images each with a certain prior probability and you generate Earth models with TI1 and Earth models with TI2

## Slide 26: Formalizing the decision problem
Decisions are based on alternatives defined by taking different actions a (drill at A or drill at B or…)
Response functions ga are used to predict the outcome of these actions (e.g. flow simulation) on Earth models

## Slide 27: Formalizing the decision problem
Comparing alternatives is based on value: what is the value of the predicted action (what is the value of drilling at location A,B etc…)
Since Earth models are uncertain, value is uncertain, we take the expected value to make a decision

## Slide 28: Formalizing the decision problem
which one has the maximum value ?
mathematically we write this as follows

## Slide 29: Case study: modeling uncertainty
- 45º
0º
45º
- 45º
0º
45º
45º
0º
- 45º
Mixed
Northwest
Southwest
q1
q2
q3

## Slide 30: Definition of value
Salinity in the groundwater in an area will eliminate the potential of growing crops
A threshold is defined on salinity content of water in the subsurface and used to determine whether that area can yield crops
That yield gets equated in dollars
Most important: determining the salinity requires flow simulation

## Slide 31: Alternative actions
Drill wells and inject water to replenish the groundwater table and drive out the salt water
Propose three location for such recharge = three different actions + no recharge
Loc 1
Loc 2
Loc 3
which is the best location
if we can only afford one well?

## Slide 32: Flow simulation
Flow simulation with the existing pumping wells in this area
salinity

## Slide 33: Decision tree without data

## Slide 34: The data: airborne TEM
Electrical resistivity is an indicator of clay-content

## Slide 35: Purpose of the data
Important : the data does not measure the “outcome of a decision”
The data measures an uncertain property of the Earth, in this case the uncertain parameter Q, that will impact the outcome of a decision
How reliable is the data in determining this parameter → reliability

## Slide 36: Reliability
Recall: reliability =
In this case

## Slide 37: Reliability calculation
Step 1: generate Earth models by varying Q (see above)
Step 2: on each Earth model, forward simulate the data
Step 3: on each forward simulation, interpret the data in terms of Q
Step 4: compare that interpreted Q with the original Q of step 1, namely: do you get a match ?

## Slide 38: Step 2
Earth model
Forward simulated data
Geophysics
Forward simulation
- 45º
0º
- 45º
Northwest
q2

## Slide 39: Step 3
Forward simulated data
Make an
interpretation
- 45º
0º
- 45º
Northwest
S2
Did you get back q2 ?

## Slide 40: Workflow

## Slide 41: Step 4